## Slide 1
RENEWABLE ENERGY • PREDICTIVE MAINTENANCE
Predictive Maintenance of Solar Trackers
via Motor Current Signature Analysis (MCSA)
Current Acquisition → Signal Processing → Feature Extraction → Fault Detection → Maintenance Alert

## Slide 2
CONTENTS
01. Introduction
05. Findings
02. Background
06. Discussion
03. Objectives
07. Reflection
04. Methodology
08. Conclusion

## Slide 3
01
Introduction
Solar PV plants increasingly rely on single/dual-axis trackers to boost energy yield.
Tracker motors and gear mechanisms are naturally prone to wear-related faults.
Undetected motor faults reduce tracking accuracy, power output, and increase maintenance cost.
This project applies Motor Current Signature Analysis (MCSA) — a non-invasive technique — to detect tracker motor faults early.
PROJECT SNAPSHOT
DOMAIN
Renewable Energy & Predictive Maintenance
TECHNIQUE
Motor Current Signature Analysis (MCSA)
TARGET
Single/Dual-Axis Solar Tracker Motors
PROCESSING
FFT, DWT, Statistical Feature Extraction
Introduction
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 4
02
Background & Motivation
The growing deployment of solar PV plants has made trackers essential for maximizing energy generation — but motor and gear failures threaten that gain.
1
Solar trackers operate continuously under varying environmental conditions.
2
Mechanical wear gradually affects motor performance over time.
3
Unexpected motor failures reduce plant availability and revenue.
4
MCSA enables non-invasive fault monitoring using existing current signals.
5
Early fault detection reduces downtime and maintenance costs.
6
Predictive maintenance improves overall system reliability and energy yield.
Background
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 5
03
Objectives
To develop a predictive maintenance system for solar tracker motors using Motor Current Signature Analysis (MCSA) for early fault detection and maintenance scheduling.
Design a laboratory-scale solar tracker monitoring system.
Acquire motor current using a Hall-effect current sensor.
Perform Motor Current Signature Analysis on the acquired data.
Extract diagnostic features from current signals (FFT / DWT / statistical).
Detect abnormal motor operating conditions.
Generate maintenance alerts before failure occurs.
Improve tracker reliability while minimizing maintenance cost.
Objectives
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 6
Research Questions & Gap
RESEARCH QUESTIONS
Can motor current signatures accurately identify faults in solar tracker motors?
Which signal processing technique (FFT, DWT, Statistical Features) gives better fault detection performance?
Can early-stage mechanical faults be detected before complete motor failure occurs?
How effectively can predictive maintenance improve tracker system reliability?
RESEARCH GAP
Most existing studies focus on PV panel-level faults; tracker motor health monitoring gets limited attention.
Existing predictive maintenance mostly uses vibration/temperature sensors — higher cost, more complex installation.
MCSA application to solar tracker motor fault diagnosis is still limited in literature.
Few studies offer a real-time, low-cost predictive maintenance framework specifically for tracker mechanisms.
Research Questions & Gap
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 7
04
Methodology — System Block Diagram
Methodology
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 8
04
Methodology — Process Stages
1
The solar tracker motor operates under normal tracking conditions.
2
Motor current is continuously measured using an ACS712 current sensor.
3
The analog signal is conditioned and digitized using an ADC (ADS1115).
4
Current data is acquired through an ESP32 / STM32 microcontroller.
5
Motor Current Signature Analysis is performed using FFT / DWT.
6
Fault-related features — harmonic components, RMS, frequency peaks — are extracted.
7
A fault classification algorithm determines the motor's health condition.
8
Maintenance alerts are generated whenever abnormal conditions are detected.
Methodology
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 9
Hardware & Software Requirements
Component / Software | Purpose
MATLAB / Simulink | Signal processing & simulation
Arduino IDE | Microcontroller programming
ESP32 / STM32 | Data acquisition
ACS712 Current Sensor | Motor current measurement
ADS1115 ADC | Signal digitization
DC / BLDC Motor | Solar tracker actuator
Motor Driver | Motor control
Power Supply | System operation
WHY THESE COMPONENTS?
Low-cost: total hardware under ₹10,000
Non-invasive: current sensor only, no vibration/temperature hardware
Edge-capable: ESP32/STM32 process signals in real time
Hardware & Software
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 10
Cost Estimation & Timeline
COST ESTIMATION
Component | Approx. Cost (₹)
ESP32 Development Board | 700
ACS712 Current Sensor | 250
ADS1115 ADC | 300
Motor Driver | 500
DC / BLDC Motor | 2,000
Mechanical Tracker Prototype | 3,500
Power Supply | 800
Miscellaneous Components | 1,000
Total Estimated Cost | ≈ 9,050
PROJECT TIMELINE (6 MONTHS)
Month 1
Literature Survey & Research Paper Review
Month 2
Problem Definition & System Design
Month 3
MATLAB / Simulink Model Development
Month 4
MCSA Implementation & Feature Extraction
Month 5
Simulation Testing & Performance Analysis
Month 6
Documentation & Software Validation
Cost & Timeline
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 11
Literature Survey
11 papers reviewed — base papers, MCSA/ML techniques, and solar PV predictive maintenance

## Slide 12
Literature Survey
Part 1 of 3 — Papers 1–4
# | Title & Year | Key Contribution | Demerit
1 | Machine Learning for PV Single Axis Tracker Fault Detection and Classification (Base Paper 1) (2025) | Real-time ML framework (XGBoost Predictor + Classifier) detects and classifies SAT Stall & Timing Mismatch faults with near-zero false positives. | Detects only software/tracking faults, not motor-level mechanical wear.
2 | An Autoregressive-Based MCSA Approach for Fault Diagnosis of Electric Motor-Driven Mechanisms (Base Paper 2) (2025) | Combines wavelet transform with autoregressive spectral estimation; defines a SISSD health indicator for motor-driven mechanism fault diagnosis. | Fault severity isolation was unreliable in several test configurations.
3 | Condition Monitoring of Bearing Damage — A Benchmark Data Set for Data-Driven Classification (2016) | Released a widely-used, labeled benchmark dataset of motor current signals for bearing-fault classification research. | Data from constant-speed industrial motors, not intermittent tracker operation.
4 | Motor Current Signature Analysis for Fault Detection of Induction Machine — A Review (2021) | Consolidates time- and frequency-domain MCSA techniques for induction machine fault interpretation. | Purely a review with no experimental validation.
Literature Survey
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 13
Literature Survey
Part 2 of 3 — Papers 5–8
# | Title & Year | Key Contribution | Demerit
5 | A Deep Autoencoder-Based CNN Framework for Bearing Fault Classification in Induction Motors (2021) | Semi-supervised DAE + 1-D CNN pipeline achieves bearing-fault classification accuracy exceeding 99%. | Computationally heavy, not optimized for low-power edge devices.
6 | Improved CNN-Based Bearing Fault Diagnosis Using Multi-Phase Motor Current Signals (2025) | Multi-phase CNN (MI-CNN) achieves ~95.12% accuracy on noisy current signals at 20 dB SNR. | Requires multi-phase current access, unavailable on many tracker motors.
7 | Robust MCSA-Based Fault Detection Under Varying Operating Conditions (2022) | Beamforming-based spectral estimation robustly detects faults under varying load and noisy conditions. | Validated on only a single fault type (minor eccentricity).
8 | Induction Motor Bearing Fault Classification Using DNN with PSO-XGBoost (2024) | Hybrid statistical + deep-learning features with PSO-optimized XGBoost improve classification accuracy. | Complex hybrid pipeline relying on vibration-based benchmark comparisons.
Literature Survey
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 14
Literature Survey
Part 3 of 3 — Papers 9–11
# | Title & Year | Key Contribution | Demerit
9 | A Motor Current Signal Based Bearing Fault Diagnosis Using Deep Learning and Information Fusion (2019) | Fuses motor current with drive DC current using deep learning for improved fault detection confidence. | Requires extra drive-level DC current sensing, increasing cost.
10 | Faults, Failures, Reliability, and Predictive Maintenance of Grid-Connected Solar Systems: A Review (2025) | Reviews PV fault taxonomy and shows AI/ML/IoT approaches enhance predictive diagnostics over reactive methods. | General PV review; no focus on tracker motors specifically.
11 | AI-Based Predictive Maintenance of Solar Photovoltaic Systems: A Comprehensive Review (2025) | Structured review of 40 papers on ML/DL-based PV predictive maintenance, evaluated via standard metrics. | Focused on panel/inverter-level maintenance, not tracker motor health.
Literature Survey
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 15
05
Findings (Expected Outcomes)
✓
Detect motor faults during the early stages.
✓
Improve the reliability of solar tracking systems.
✓
Reduce unexpected tracker failures.
✓
Minimize maintenance cost through condition-based maintenance.
✓
Increase operational efficiency of photovoltaic plants.
✓
Improve energy generation by maintaining accurate panel tracking.
✓
Demonstrate a practical, low-cost predictive maintenance solution.
Findings
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 16
06
Discussion
SIGNAL PROCESSING TECHNIQUE COMPARISON
Technique | Strength | Trade-off
FFT | Fast, simple frequency-domain view of steady current | Poor with non-stationary / transient signals
DWT | Captures both time and frequency information | Higher computation, filter/level selection needed
Statistical Features | Lightweight (RMS, peaks); easy to compute on edge devices | Less sensitive to subtle, early-stage faults
WHY MCSA OVER VIBRATION / TEMPERATURE SENSING?
Uses the motor's own current — no extra vibration or temperature hardware needed
Lower cost and simpler installation than multi-sensor condition monitoring rigs
Fits the project's low-cost, real-time, edge-deployable design goals
Discussion
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 17
07
Reflection
WHAT WORKED WELL
Low-cost setup using a single current sensor
No extra vibration/temperature hardware required
Real-time, edge-deployable microcontroller pipeline
CHALLENGES FACED
Collecting clean, representative fault data
Filtering noise from real-world current signals
Emulating realistic fault conditions safely
WHAT WE'D IMPROVE
Test more fault types and severities
Longer real-world / field testing duration
Compare more signal processing techniques
Reflection
MCSA-Based Predictive Maintenance for Solar Trackers

## Slide 18
08
Conclusion
A low-cost, non-invasive MCSA-based predictive maintenance system is proposed for solar tracker motors.
The system captures motor current, processes it (FFT/DWT), and extracts features to detect faults early.
Expected to reduce downtime, cut maintenance costs, and improve solar plant reliability and energy yield.
Future work: field deployment on live trackers and integration with SCADA/IoT monitoring dashboards.
Thank You